## Slide 1
DC Opportunity
Sochaux
Confidential

## Slide 2
Location
Comments
Distance from Strasbourg: 120 km Distance from Frankfurt am Main: 320 km Distance from Paris: 360 km
https://www.google.com/

## Slide 3
Landplot
Comments
Land plot: c. 35 ha

## Slide 4
Pas de risque aérien
Airports
Comments
Land plot outside any aeronautical easement

## Slide 5
Connectivity
Comments
The site is very close to major fiber backbone (50 m distance)

## Slide 6
Comments
The site offers diversified power connection options 1 – 63KV substation (450 m distance) 2 – Étupes 225KV substation (1.9 km distance) 3 – Héricourt 225KV substation (6 km distance)
Power environment
1
2
3

## Slide 7: Environmental Risks

## Slide 8
Technological & Chemical Risk
Comments
No SEVESO high-threshold sites in close proximity <1.5 km
*^*

## Slide 9
Technological Risks
Comments
Land plot mainly impacted by hydrocarbon and gas pipeline

## Slide 10
Flood risk
Comments
Land plot 100% within the pipeline prescription zone Flood reference level (PPRi) ≈ 319.4 m NGF Target: ground floor set at 320 m NGF (reference level + safety margin)

## Slide 11
Soil
Comments
Marls containing Helix and Mytilus, sandstone, conglomerates and lacustrine limestones (Ludian) Recent undifferentiated alluvial deposits, gravel, sand and clay

## Slide 12: Local urban development analysis (PLU)

## Slide 13
PLU analysis
Comments
Land plot located in UZ and UYb areas UZ : Industrial estate UYb : Sites intended primarily for industrial activities

## Slide 14
PLU analysis
Comments: UZ area
Footprint: No specific floor area Height: max 25 m

## Slide 15
PLU analysis
Comments: UYb area
Footprint: unregulated Height: max 40 m

## Slide 16: Macro Sizing

## Slide 17
PLU analysis
Comments: Considering gas prescription zone
Land plot: c. 35 ha land area DC building: 62 500 sqm footprint 1 level building 7 m with 5 m technical roof IT load per building: 250 MW Total power per building: 350 MW Landplot total: 350 MW
DC
RTE
RTE
UZ
UYb