## Slide 1
DC Opportunity
Sochaux
Confidential

## Slide 2
Location
Comments
Distance from Strasbourg: 120km Distance from Franfurt am Main: 320km Distance from Paris: 360km

## Slide 3
Landplot
Comments
Landplot: c. 35 ha

## Slide 4
Pas de risque aérien
Airports
Comments
Landplot outside any aerodrome servitude

## Slide 5
Connectivity
Comments
The site is very close to major fiber backbone (50m distance)

## Slide 6
Comments
The site offers diversified power connection options 1 – 63KV substation (450m distance) 2 – Études 225KV substation (1.9km distance)
Power environment
3
1
2

## Slide 7: Environmental Risks

## Slide 8
Technological & Chemical Risk
Comments
No SEVESO high sites within 1.5 km
*^*

## Slide 9
Technological Risks
Comments
Landplot impacted by hydrocarbon and gas pipeline

## Slide 10
Flood risk
Comments
Landplot impacted by the flood area

## Slide 11
Soil
Comments
Marls containing Helix and Mytilus, sandstone, conglomerates and lacustrine limestones (Ludian) Recent undifferentiated alluvial deposits, gravel, sand and clay

## Slide 12: Local urban development analysis (PLU)

## Slide 13
PLU analysis
Comments
Landplot located in UZ and UYb area UZ : Industrial estate UYb : Sites intended primarily for industrial activities

## Slide 14
PLU analysis
Comments: UZ area
Footprint: No specific floor area Height: max 25m

## Slide 15
PLU analysis
Comments: UYb area
Footprint: unregulated Height: max 40m

## Slide 16: Macro Sizing

## Slide 17
PLU analysis
Comments
Landplot: c. 35 ha land area DC Building : 210 000sqm 1 level building 7m with 5m technical roof Data Hall : 105 000 sqm IT Load :250 MW PUE : 1,4 Total Power : 350 MW
DC 1
RTE
RTE
UZ
UYb
DC 3
DC 2